MACMACH INSTALLATION NOTES

                          Carnegie Mellon University
                             Pittsburgh, PA 15213
                                19 March 1993

1. Introduction

MacMach is a complete system using the Mach 3.0 micro kernel and UX single
server combination.  This is the first release of MacMach.  It comes with
complete sources.

The programs and libraries come from the 4.3BSD-TAHOE release.  Other items
included are the Mach specific programs, X11R4 and GNU C.

This release requires the recipient to have aa MacMach End-User license 
from Carnegie Mellon University and a BSD4.3 license form the University of
California which in turn requires either a UNIX/32V, SYSTEM III or SYSTEM V
source license from AT&T.

All of the releases that are made by CMU are done via an internet transfer
protocol called "SUP" (Software Update Protocol).  MacMach uses a program
called "newsys" to handle the issues of file system creation and calling SUP.

This document assumes a working knowledge of the installation and maintenance
for a 4.3BSD system.  If you are unfamiliar with the 4.3BSD system, you should
read the system maintainers documentation for 4.3BSD.

2. Hardware Requirements for MacMach

MacMach currently runs on the following Apple Macintosh computer systems:
Macintosh II, Macintosh IIx, Macintosh IIcx, Macintosh IIci, Macintosh IIfx,
Macintosh SE/30

MacMach on a Macintosh II must have the PMMU chip installed.
MacMach on a Macintosh IIci can not use the internal on-board viedo.

Systems can run versions 6.08 or 7.O of the Macintosh operating system.

Systems must have at least 8MB of ram.  16MB is better.
MacMach on a MacIIcx or SE/30 with 7.0 and MODE32 is limited to 8MB of ram.

MacMach requires from 30MB to 600MB of disk space depending on configuration.
30MB is the minimum bootable system.
80MB is a full system without much user space.
400MB is a full system with sources.
600MB is a complete system that can recompile itself.

MacMach needs an ethernet card.  It can run without one, but the installation
requires network access.  Note that if an ethernet card is installed, it must
be enabled by the networks control panel and chooser before MacMach will boot.

3. Installing MacMach
a) verify that you have the appropriate licenses
b) verify that your site has internet access to CMU
c) verify that your hardware is sufficient
d) send a request for MacMach to "MACH@CS.CMU.EDU".  You will be sent a
   copy of the MacMach End-User license which you must sign and return, along
   with a copy of your Unix license.  Also include your machine's internet
   address and a SUP CRYPT.  You should choose your own CRYPT, a character
   string at least 6 characters long or we will assign a random one.  Include
   a blank, high density floppy.
e) You will then receive a floppy that contains everything you need to install
   and run MacMach.  Print out the teachtext documents from the floppy and
   follow their instructions.

4. The MacMach floppy disk.
The MacMach floppy contains a couple of teachtext documents and two items to
drop into the system folder.  The documents have detailed instructions on
the Mach control panel and system installation.